PERFORMANCES OF CASCADE COMPLEX FSK-ASK  TELECOMMUNICATION SYSTEM

PERFORMANSE KASKADNE VEZE FSK-ASK SLOŽENOG TELEKOMUNIKACIONOG SISTEMA

Borivoje Miloševiæ, Zoran Milivojeviæ, Viša tehnièka škola, Niš
Marijana Miliæeviæ, Elektronski fakultet, Niš

Abstract – The aim of this paper is to determinate error probability one of the variants of  complex ASK-FSK telecommunication system when Gaussian noise, Rayleigh fadine and narrowband noice are present.

Sadržaj – Cilj ovog rada jeste odreðivanje verovatnoæe greške jedne od varijanti složenog ASK-FSK telekomunikacionog sistema, pri èemu se pretpostavlja da su prisutni Gausov šum, Rejlijev feding i uskopojasne smetnje.

1. INTRODUCTION

In real channels, such as radio, satellite and mobile channels, transfer errors are mostly caused in power changing of received signal. This is explained as fading.

In fields of cellulare mobile radio signals, buildings enviroments (such as houses, trees and buildings) behaves as reflectors of radio signals.

These obstacles produce amplitudes and phases which are weak. If the transmit is signal modulated, than multiple reflected waves arrive in recieved antenna from differents directions with different time of arrival. These reflected waves are called the waves multiple paths. Because for the presece of different time and angle arrival, waves multiple paths will have diffrents phases into received side. On received antenna, sum of waves from any place in field can make constructive or destructive signal [1]. Amplitude fluctuation of received signal is fading signal.

2. FUNCTION ANALYSIS

The observed complex telecommunication system is composed of a part for ASK and coherent FSK detection. Complex ASK-FSK system is shown on the figure:

Figure 1. Model complex ASK-FSK system

Transmit wave is binary signal, and it has next form [2]:

(1)

After amplitude modulation, signal passes through frequency modulation.

It is introdused four form of signal after modulation, and  on next way : , when transmit information is in form 00, , when transmit information is in form 01, , when transmit information is in form 10, and , when transmit information is in form 11.

Form  and  will be considered in case , and form  and  in case .

To describe detailed analyses, it begins from case  and it observes situation when signal is in form:

.

On input of filtar white Gaussian noise is added with zero main value, and variance  and narrowband noise [1]:

where are  and  statistics independent Gaussian variables with zero main value and variance . Phases  and  have uniform distribution

(2)

and since the signal is transmited over free space by transmitter to receiver, it will be considered that Rayleigh fading is present so that the amplitudes have Rayleigh distribution.

(3)

Signal will be followed through system to the output of transmitter:

(4)

Passing through filtar with central frequency  it is obtained:

(5)

Now, signal is multipled with carrier frequency, and it is obtained

(6)

Passing by other filtar it is obtained:

(7)

Because signal  passes through free space, it is considered that Rayleigh fading is present and his envelop will have this form:

(8)

Now, it is integrated with  and :

(9)

Figure 1. showes the envelop of signal . After that signal is frequently modulated and it is obtained

(10)

On input of the receiver is present white Gaussian noise. In this case will be considered two hypothesis:

Here is the case where the hypothesis  is achieved. In upper branch signal has form:

(11)

and after multipling with carrier frequency

(12)

in that way into upper branch putput signal here is

(13)

In lower branch there is next situation

(14)

after multipling with carrier frequency

(15)

in that way into lower branch there is

(16)

Output signal is

(17)

Now, it is

(18)

where  and  are known from previous estimation and  [2]. After integrating with  and  envelop of output signal is obtained when the hypothesis is achieved

(19)

Figure 2. shows the envelop of signal  when hypothesis is achieved.

Here is the case where is hypothesis achieved.

(20)

after multipling with carrier frequency

(21)

in that way into upper branch there is

(22)

In lower branch there is next situation

(23)

and after multipling with carrier frequency

(24)

in that way into upper branch there is

(25)

Output signal is

(26)

Now, it is

(27)

where  and  are known and . Here is the distribution of the envelop when is hypothesis  achieved

(28)

Figure 3. shows envelop signal  when hypothesis  is achieved.

Now, the case  is considered. The signal has this form

(29)

As in previous case, the signal will be followed to the output of transmmiter:

(30)

Passing through filtar with central frequency , it is obtained

(31)

Now, signal is multiplied with carrier frequency and it is obtained

(32)

Again, passing through filtar, the signal has this form:

(33)

and envelop will have form on receiving:

(34)

it is integrated by  and

(35)

Figure 4. shows the envelop of signal .

Signal is modulated and it is obtained

(36)

On the input of the receiver white Gaussian noise is present. In this case two hypothesis will be consider:

In the case when hypothesis  is achieved:

(37)

after multpling with carrier frequency

(38)

so in upper input branch there is

(39)

In lower branch is this situation

(40)

after multipling with carrier frequency

(41)

and in upper branch there is

(42)

Output signal is

(43)

Now, it is

(44)

where  and  are known. This is the distribution of the envelop,  when the hypothesis  is achieved

(45)

Figure 5. shows envelop of signal  when hypothesis  is achieved.

When hypothesis  is achieved

(46)

after multipling with carrier frequency

(47)

that is in upper output branch

(48)

In lower branch there is

(49)

after multipling with carrier frequency

(50)

so in lower output branch there is

(51)

Output signal is

(52)

Now, it is

(53)

where  and  are known. This is the distribution when the hypothesis  is achieved

(54)

Figure 6. shows the envelop signal  when the hypothesis  is achieved.

Total error probability is

(55)

3. RESULTS

Figure 1. illustrates the envelop signal  for case  with ,  and .

Figure 1. Envelop signala  for case  with ,  i .

Figure 2. illustrates the envelop signal  for hypothesis  with .

Figure 2. Envelop signal

Figure 3. illustrates envelop signal  for hypothesis  with .

Figure 3. Envelop signal

Figure 4. illustrates the envelop signal  for case  with ,  and .

Figure 4. Envelop signal

Figure 5. illustrates the envelop signal  for hypothesis  with .

Figure 5. Envelop signal

Figure 6. illustrates the envelop signal  for hypothesis  with .

Figure  6. Envelop signal

Figure 7. illustrates the total error probability of the whole system.

Figure 7. Characteristic of the total error probability of system

4. CONCLUSION

In this paper, the complex telecommunication system is described with combination for modulation coherent ASK and FSK. Bipolar signal is brought to the input of receiver, which is modulated with ASK and then FSK. His considered that Rayleigh fading are present, Gaussian noise and narrowband noise. On the ground, coherent FSK detection is filtered and the results from the distributions of the envelopes are given in certain parts of the system.

REFERENCES

[1] Stefanoviæ M., Performances of digital telecommunication systems, Faculty of electrical engineering Nish

[2] Stefanoviæ M., Detection of signal with white and colored Gaussian noise, Faculty of electrical engineering Nish

[3] Biglieri B., Principles of digital communications