OPTIMALNO PODEŠAVANJE PI/PID REGULATORA ZA PROCESE

DEFINISANE RACIONALNOM FUNKCIJOM PRENOSA

Tomislav B. Šekara, Miroslav R. Mataušek, Elektrotehnički fakultet u Beogradu

Sadržaj - U radu je razvijen postupak optimizacije PI/PID regulatora zasnovan na minimizaciji JISE kriterijuma, za procese definisane racionalnom funkcijom prenosa. Izvršena je uporedna analiza sa najboljim do sada razvijenim metodama za podešavanje PI/PID regulatora. Pokazano je da predložena metoda, u odnosu na prethodne,  kvalitativno potvrđuje ili poboljšava performanse sistema u zatvorenoj povratnoj sprezi (SAU) i daje fizičko tumačenje optimizacione procedure zasnovane na maksimizaciji proporcionalnog pojačanja PI/PID regulatora.

Abstract – A new procedure, based on the minimization of JISE,, is developed for obtaining an optimal and robust tuning of PI/PID controller. It is assumed that the process dynamics can be characterized by a rational transfer function. Comparison with the best optimization methods proposed until now confirms the effectivenes of the proposed method.

Ključne riječi – PID regulator, Optimizacija, Robusnost

Key words –PID controller, Optimization, Robustness

1.	UVOD

Danas postoje mnoge metode za određivanje prihvatljivih parametara PI/PID regulatora. Metode se razlikuju u složenosti, fleksibilnosti i zahtjevanom apriornom znanju o procesu. Prema [1] oko 94% povratnih sprega u industriji realizovano je preko PI/PID regulatora, a istraživanje [2]  je prema [3] pokazalo da u petrohemijskoj industriji taj procenat iznosi preko 97%. Ovakav značaj PI/PID regulatora bio je i motiv za razvoj dvije efikasne i jednostavne procedure za podešavanje parametara industrijskih regulatora [4,5]. Posljednjih godina je razvijeno [6-11] više optimizacionih procedura kojima se parametri PI/PID regulatora podešavaju tako da se minimizira IAE (Integrated Absolute Error) pri ograničenjima na robusnost, što zadovoljava kriterijum Shinskeyog [12], po kom kvalitetan industrijski regulator mora da bude podešen tako da, na step poremećaj na ulazu, daje minimum IAE i minimum maksimalnog odstupanja  izlaza od nominalnog režima uz ograničenja na robusnost. Konačno treba pomenuti i mogućnost primjene savremenih metoda optimizacije kao što je  (mixed sensitivity) [13], kao i podešavanje PI/PID regulatora primjenom frakcionog prilaza [14-18].

U ovom radu se razmatra optimizacija PI/PID regulatora zasnovan na minimizaciji JISE kriterijumu kao i uporedna analiza predložene sa najboljim do sada razvijenim metodama za podešavanje PI/PID regulatora. Pokazano je da predložena metoda kvalitativno potvrđuje ili poboljšava performanse sistema u zatvorenoj povratnoj sprezi (SAU): manji IAE i a robusnost  je zagarantovana zahtjevom da maksimum osjetljivosti bude manji ili jednak zadatoj vrijednosti Ms .

Niz metoda [6-11] zasniva se na maksimizaciji integralnog pojačanja ki. Naime, ako je signal greške na jedinični step signal poremećaja pozitivan tada je

.				(1)

U opštem slučaju prethodna relacija ne daje najbolje rješenje u smislu optimizacione procedure PID regulatora [7]. Dodavanjem podešljivog parametra  ovakva optimizaciona procedura (maksimizacija integralnog pojačanja ki) je poboljšana u smislu postizanja boljih performansi u radu [11]. Osim toga u radu [11] su, uvođenjem nove optimizacione procedure (maksimizacija proporcionalnog pojačanja k), za iste podešljive parametre , postignute najbolje performanse u odnosu na druge optimizacione procedure [6-10]. Kroz niz simulacija na tipičnim procesima izvršeno je poređenje optimizacione procedure zasnovane na minimizaciji JISE kriterijuma sa optimizacionom procedurom zasnovanom na maksimizaciji proporcionalnog pojačanja k [11] i uočena je kvalitativna sličnost. Ovim je optimizaciona procedura zasnovana na maksimizaciji k dobila fizičko tumačenje, što takođe predstavlja jedan od doprinosa ovoga rada.

2.	OPTIMIZACIONA PROCEDURA ZASNOVANA

NA  MINIMIZACIJI JISE KRITERIJUMA

Da bi primijenili sljedeću optimizacionu proceduru za određivane optimalnih parametara PI/PID regulatora, neophodno je analitički odrediti JISE (Integral of squared error) u funkciji podešljivih parametara regulatora. U opštem slučaju JISE  je definisan relacijom

,		(2)

gdje je  Laplaceova transformacija signala greške . Rešenje prethodnog integrala kada je funkcija racionalna

,				(3)

može se odrediti analitički [19], tako da je:

.						(4)

Matrice  se formiraju u zavisnosti stepena  polinoma . Ako je stepen  neparan broj tada je matrica  definisana relacijom

.	(5)

Ako je stepen  paran broj tada je  dato sa

.	(6)

Matrica  formira se na isti način, tako da se za  neparno zadnja vrsta matrice  zamjenjuje sa vrstom koeficijenata  a ako je  parno treba prvu vrstu matrice  zamijeniti sa koeficijentima , koji su definisani relacijom

.	(7)

Odaberimo upravljačku sruktura sa PID regulatorom prikazanu na slici 1, koju je predložio Åström [7]

Slika 1. Upravljačka struktura sa PID regulatorom

Funkcija povratnog prenosa ovakve upravljačke strukture je

.		(8)

Za stabilne procese upravljanja u odnosu na zadati podešljivi parametar  data je Nyquistova kriva na slici 2. koja u tački  tangira zadati krug poluprečnika  sa centrom u tački . Prema [7], vremenska konstanta filtra  je .

Slika 2. Nayquistov dijagram  u odnosu na zadato

U [6,7] u cilju postizanja željenih performansi SAU kao podešljivi parametri usvajaju se: , . U radu [11] uveden je još jedan podešljivi parametar  koji po prirodi predstavlja faktor relativnog prigušenja nule PID regulatora a definiše se kao

.						(9)

Tako na primjer kod Ziegler-Nicholsove procedure , što odgovara . Ako diferencijalno dejstvo PID regulatora izrazimo u funkciji podešljivog parametra , dobija se

.							(10)

Tada optimizaciona procedura dobija sljedeću formu:

Neka je uz relacije (8) i (10) definisana i funkcija  kao

.			(11)

Odredimo minimum kriterijuma performanse JISE

(12)

pod ograničenjima

,						(13)

,					(14)

.					(15)

Rješavanjem (11)-(15) dobijaju se optimalni parametri PI/PID regulatora

(16)

odnosno

i .		(17)

Podešljivi parametri su maksimalna osjetljivost , uticaj filtra šuma  i prigušenje , o kome će biti riječi u sljedećem poglavlju 3.

3.	REZULTATI SIMULACIJE

Za dva procesa, korišćena i u [7,9,11], analizirana je predložena metoda zasnovana na minimizaciji JISE. Detaljno upoređenje sa najboljim do sada razvijenim metodama prikazano je na slikama  Sl. 4 i Sl. 5 i pokazuje sličnost sa metodom zasnovanom na maksimizaciji k [11] a značajnu prednost u odnosu na metodu zasnovanu ma maksimizaciji ki [7,11]. Konačno, slikama Sl. 3a i Sl. 3b ilustrovana je prednost metoda zasnovanih na maksimizaciji k [11] i minimizaciji JISE u odnosu na do sada, za ova dva procesa, najbolji rezultat postignut u svijetu [9].

a)

b)

Slika 3. Odzivi na poremećaj optimalno podešenog PID regulatora, za procese Gp1(s)  i Gp2(s), primjenom:

metode Kristiansson-Lennartson (KL), maximizacije k (ŠEMA 1) i minimizacije JISE  (ŠEMA 2)

Na slikama Sl. 3a i Sl. 3b sa ŠEMA 1 i ŠEMA 2 označeni su respektivno PID regulatori dobijeni metodama predloženim u [11] (ŠEMA 1) i u ovom radu (ŠEMA 2). Rezultati na ovim slikama, kao i rezutati na slikama Sl. 4 i Sl 5 potvrđuju sličnost rezultata koji se dobijaju predloženim metodama, ŠEMA 1 i ŠEMA 2, kao i njihovu prednost u odnosu na metodu zasnovanu na maksimizaciji ki predloženu u [7].

a)

b)

c)

Slika 4. Uporedna analiza optimalnog podešavanja PID regulatora, za proces Gp1(s) zasnovanog na:

a) minimizaciji JISE ,  b) maximizacija k i c) maximizacija ki

a)

b)

c)

Slika 5. Uporedna analiza optimalnog podešavanja PID regulatora, za proces Gp2(s) zasnovanog na:

a) minimizaciji JISE ,  b) maximizacija k i c) maximizacija ki

4.	ZAKLJUČAK

Predložena nova metoda optimalnog podešavanja PI/PID regulatora pokazala se izuzetno efikasnom. Osim toga, njenom primjenom, i uporednom analizom sa metodom zasnovanom na maksimizaciji k obje metode dobile su praktično isto fizičko tumačenje, što takođe predstavlja doprinos ovoga rada. Konačno, obje metode su efikasnije od metode zasnovane na maksimizaciji ki.

REFERENCE

[1]	S. Yamamoto and I. Hashimoto, "Present status and future needs: the view from Japanese industry", In Arkun and Ray, Eds., Chemical Process Control-CPCIV. Proc. 4th Inter. Conf. on Chemical Process Control, TX, 1991.

[2]	L. Desbourough, R. Miller, "Increasing customer value of industrial control performance monitoring––Honeywell’s experience", in: Sixth International Conference on Chemical Process Control, AIChE Symposium Series Number 326, Vol.. 98, 2002.

[3]	K. J. Åström, T. Hägglund, "Revisiting the Ziegler–Nichols step response method for PID control", Journal of Process Control, Vol. 14, pp. 635–650, 2004.

[4]M. R. Mataušek, G. S. Kvaščev, "A unified step response procedure for autotuning of PI controller and Smith predictor for stable processes", Journal of Process Control, Vol. 13, pp. 787-800, 2003.

[5]S. Skogestad, "Simple analytic rules for model reduction and PID controller tuning", Journal of Process Control, Vol. 13, pp. 291–309, 2003.

[6] K. J. Åström, H. Panagopoulos and T. Hägglund, "Design of PI controllers based on non-convex optimization", Automatica, Vol. 34, pp. 585-601, 1998.

[7]	H. Panagopoulos, K. J. Åström and T. Hägglund, "Design of PID controllers based on constrained optimization", IEE Proc-Control Theory Appl., Vol. 149, pp. 32-40, 2002.

[8]	C. Hwang, C-Y. Hsiao, Solution of non-convex optimization arising in PI/PID control design, Automatica, Vol. 38, pp. 1895-1904, 2002 .

[9]	B. Kristiansson, B. Lennartson, "Evaluation and simple tuning of PID controllers with high-frequency robustness", Journal of Process Control Vol. 16, pp. 91-102, 2006.

[10] A. Karimi, M. Kunze, R. Longchamp, "Robust controller design by linear programming with application to a double-axis positioning system", Control Engineering Practice, Vol. 15, pp. 197-208, 2007.

[11] T. B. Šekara, M. R. Mataušek, "A simple effective method to obtain a well-tuned PID controller", Journal of Process Control, Submited Paper, 2006.

[12] F. G. Shinskey, "How good are our controllers in absolute performance and robustness?", Measurement and Control, Vol. 23, pp. 114–121, 1990.

[13] S. Skogestad, I. Postlethwaite, Multivariable Feedback Control, Wiley, 1996.

[14] T. B. Šekara, Frakcione transformacije sa primjenom u sistemima automatike i električnim kolima, Doktorska disertacija, Elektrotehnički fakultet Univerziteta u Beogradu, 2006.

[15] I. Podlubny, "Fractional-Order Systems and  controllers", IEEE Trans. AC, Vol. 44, pp. 208-214, 1999.

[16] H. F. Raynaud and A. Zergaïnoh, "State-space representation for fractional order controllers", Automatica, Vol. 36, pp. 1017-1021, 2000.

[17] C. A. Monje, A. J. Calderon, B. M. Vinagre, Y. Q. Chen and V. Feliu, "On Fractional  Controllers: Some Tuning Rules for Robustness to Plant Uncertainties", Nonlinear Dynamics, Vol.38,pp. 369-381, 2004.

[18] T. B. Šekara, M. R. Mataušek, "Frakciono dinamičko proporcionalno dejstvo PI/PID regulatora", Zbornik radova L Konf. ETRAN, Vol. 1, pp. 252-255, 2006.

# [19] C. Schmid, Course on dynamics of multidisplicinary and controlled systems, http://www.atp.ruhr-uni-bochum.de/rt1/syscontrol/

OPTIMAL TUNING OF PI/PID CONTROLLER FOR PROCESSES DEFINED BY RATIONAL TRANSFER FUNCTION

Tomislav B. Šekara and Miroslav R. Mataušek