UPOREDNA ANALIZA DVIJE METODE ZA OPTIMALNO PODEŠAVANJE

PID REGULATORA ZA NESTABILNE PROCESE

PARALLEL ANALYSIS TWO METHODES OF OPTIMAL  SETTINGS

PID CONTROLLERS FOR UNSTABLE PROCESES

Slobodan Vukosavljević, Marija Močević, ETF Istočno Sarajevo

e-mail: slobodanv@teol.net ; m_mocevic@yahoo.com

Sadržaj - U ovom radu je predstavljena analiza dvije metode za optimalno podešavanje PID regulatora za nestabilne procese. Metode se odnose na maksimizaciju parametara regulatora  ki i k. Maksimizacija ova dva parametra smanjuje integralnu apsolutnu grešku (IAE), povećava robusnost sistema i omogućava kvalitetno upravljanje nestabilnim procesom. Uticaj šuma i poremećaja na sistem je smanjen upotrebom filtra prvog reda.

Abstract –Two methods to obtain optimal settings of PID controllers for unstable process are analyzed in this paper. Methods are based on maximization of parameters k and ki. Maximization of these parameters decrease integral absolute error (IAE), increase robustness of the closed-loop system.  Effect of noise and disturbance is decreased by applying a first order filter.

Ključne riječi – PID regulator, nestabilni proces, Optimizacija, Robusnost

Key words –PID controller, unstable process, Optimization, Robustness

1.	UVOD

PID regulatori su danas najzastupljeniji upravljački algoritmi. Prema [1] oko 94% povratnih sprega u industriji realizovano je preko PI/PID regulatora, a istraživanje [2]  je prema [3] pokazalo da u petrohemijskoj industriji taj procenat iznosi preko 97%. Posljednjih godina je razvijeno mnoge različitih metode za određivanje prihvatljivih parametara PI/PID regulatora [4-11]. Metode se razlikuju u složenosti, fleksibilnosti i poznavanju procesa koji koristimo.

Ovaj rad opisuje uporednu analizu dvije metode za optimalno podešavanje PID regulatora za nestabilne procese. Prva metoda zasnovana je na maksimizaciji integralnog pojačanja  koja smanjuje integralnu apsolutnu grešku IAE (Integrated Absolute Error) i manje  a robusnost je zagarantovana zahtjevom da maksimum osjetljivosti bude manji ili jednak zadatoj vrijednosti Ms . Naime, ako je signal greške  na jedinični step signal poremećaja pozitivan tada je

.					(1)

Treba napomenuti da u opštem slučaju prethodna relacija ne daje najbolje rješenje u smislu optimizacione procedure PID regulatora [7]. Dodavanjem podešljivog parametra  ovakva optimizaciona procedura (maksimizacija integralnog pojačanja ki) je poboljšana u smislu postizanja boljih performansi u radu [11]. Druga metoda takođe razvijena u radu [11] je zasnovana na maksimizaciji proporcionalnog pojačanja k, za iste podešljive parametre . Rezultati simulacije u cilju uporedne analize obje metode su dati na jednom nestabilnom procesu.

2.	PROBLEM FORMULACIJE

Odaberimo upravljačku sruktura sa PID regulatorom prikazanu na slici 1, koju je predložio Åström [7]

Slika 1. Upravljačka struktura sa PID regulatorom

Funkcija povratnog prenosa ovakve upravljačke strukture je

.		(2)

Proces sa funkcijom prenosa  je upravljan pomoću PID regulatora. Data upravljačka struktura ima dobre karakteristike pri promjeni referentnog ulaza , reakciji na poremećaj  i filtraciji šuma .

Primarni cilj regulacione strukture je da ima dobru reakciju na pojavu poremećaja opterećenja. Najčešće korišćeni kriterijum performanse sistema je (1). Razlog što koristimo IE je taj što njegova vrijednost je obrnuto proporcionalna integralnom pojačanju regulatora, i što omogućava jednostavan model algoritma za optimalno podešavanje parametara PID regulatora. Osim toga u radu [11] su, uvođenjem nove optimizacione procedure (maksimizacija proporcionalnog pojačanja k), za podešljive parametre , postignute najbolje performanse u odnosu na druge optimizacione procedure [6-10]. Podešljivi parametri definisani su:

(3)

Za nestabilne procese upravljanja sa jednim nestabilnim polom u odnosu na zadati podešljivi parametar  data je Nyquistova kriva na slici 2. koja u tački  tangira zadati krug poluprečnika  sa centrom u tački .

Slika 2. Nayquistov dijagram  u odnosu na zadato  sa jednim nestabilnim polom

Prema [7], vremenska konstanta filtra je: prvog reda    i za filter višeg reda .

U [6,7] u cilju postizanja željenih performansi sistema automatskog upravljanja kao podešljivi parametri usvajaju se: , . U radu [11] uveden je još jedan podešljivi parametar  koji po prirodi predstavlja faktor relativnog prigušenja nule PID regulatora a definiše se kao

.						(4)

Tako na primjer kod Ziegler-Nicholsove procedure , što odgovara . Diferencijalno dejstvo PID regulatora izrazimo u funkciji podešljivog parametra , dobija se

.							(5)

U radu [11] optimizacione procedure imaju sljedeću formu:

Neka je uz relacije (2) definisana i funkcija  kao

.			(6)

Prva optimizaciona metoda zasnovana na maksimizaciji integralnog pojačanja  predstavlja rješenje ekstremuma implicitno zadate funkcije , po parametru , tj.

,						(7)

,					(8)

,					(9)

zatim zamjenom u relacije (7)-(9) i njihovim rješavanjem se dobijaju optimalni parametri PID regulatora

, , 				(10)

odnosno

i .		(11)

Druga optimizaciona metoda zasnovana na maksimizaciji proporcionalnog pojačanja  predstavlja rješenje ekstremuma implicitno zadate funkcije , po parametru ,  tj.

,						(12)

,					(13)

,					(14)

zatim zamjenom u relacije (7)-(9) i njihovim rješavanjem se dobijaju optimalni parametri PID regulatora

, , 				(15)

odnosno

i .		(16)

Prema [7], određuju se: parametar  odnosno adekvatni filter na zadatu referencu.

Interesantno je napomenuti da za nestabilne procese podešljivi parametar  treba birati iz šireg skupa nego što to važi za stabilne procese u cilju postizanja boljih performansi sistema u zatvorenoj povratnoj sprezi (SAU): manji IAE i a robusnost  je zagarantovana zahtjevom da maksimum osjetljivosti bude manji ili jednak zadatoj vrijednosti Ms .

3.	REZULTATI SIMULACIJE

Rezultati simulacije i detaljno upoređenje metoda max(ki) i max(k) prikazani su na procesu sa jednim nestabilnim polom, funkcije prenosa

.

Slika 3. Simulacioni dijagram upravljačke strukture sa PID regulatorom dat u SIMULINK-u

Na slici 4 izvršeno je upoređenje metode (ŠEMA 1) zasnovane na maksimizaciji proporcionalnog pojačanja k pod ograničenjem na Ms [11] sa metodom (SK) zasnovanom na primjeni nelinearnog programiranja na minimizaciju generalizovanog kriterijuma, koji pored IAE uključuje i varijaciju upravljačke promjenljive, pod veoma složenim nelinearnim ograničenjima [14]. Za isto Ms=3.6,  i  sa daleko jednostavnijom metodom ŠEMA 1 dobijaju se praktično isti rezultati kao sa metodom SK.

Slika 4. Odziv na step poremećaj: (- - -) metoda Šekara-Mataušek, ŠEMA 1; (___) metoda Syrcos-Kookos, SK.

Međutim, kao što se vidi iz prethodne analize, metoda SK ne garantuje prihvatljive vrijednosti pokazatelja robusnosti, Ms i Mp. S druge strane, metoda ŠEMA 1, kao što će biti pokazano, i na ovom primjeru nestabilnog sistema garantuje Ms  uz daleko bolje Mp.

U tabeli 1 i na slici 5 za zadato Ms=2 analiziran je uticaj podešljivog parametra na kvalitet regulacionog procesa za realnu vrijednost konstante filtra šuma, N=10 po metodi (ŠEMA 2) zasnovanoj na maksimizaciji integralnog pojačanja ki [11].

Tabela 1. max(ki),  i

|  | k | ki | kd |  | IAE | Mp |
| --- | --- | --- | --- | --- | --- | --- |
| 1.0 | 2.757 | 0.323 | 5.877 | 0.667 | 4.87 | 2.63 |
| 1.1 | 2.738 | 0.272 | 5.700 | 0.659 | 4.96 | 2.46 |
| 1.2 | 2.721 | 0.231 | 5.553 | 0.652 | 5.16 | 2.33 |
| 1.3 | 2.705 | 0.199 | 5.429 | 0.646 | 5.47 | 2.24 |
| 1.4 | 2.691 | 0.173 | 5.323 | 0.641 | 5.92 | 2.17 |

Slika 5. Odziv na step poremećaj u zavisnosti od podešljivog

parametra : metoda Šekara-Mataušek, ŠEMA 2.

U tabeli 2 i na slici 6 za zadato Ms=2 analiziran je uticaj podešljivog parametra na kvalitet regulacionog procesa za realnu vrijednost konstante filtra šuma, N=10 po metodi (ŠEMA 1) zasnovanoj na maksimizaciji proporcionalnog pojačanja k  [11].

Slika 6. Odziv na step poremećaj u zavisnosti od podešljivog

parametra : metoda Šekara-Mataušek, ŠEMA 1.

Tabela 2. max(k),  i

|  | k | ki | kd |  | IAE | Mp |
| --- | --- | --- | --- | --- | --- | --- |
| 0.9 | 2.913 | 0.397 | 6.605 | 0.822 | 4.28 | 2.54 |
| 1.0 | 2.913 | 0.326 | 6.501 | 0.822 | 4.31 | 2.30 |
| 1.1 | 2.913 | 0.273 | 6.422 | 0.822 | 4.48 | 2.15 |
| 1.2 | 2.913 | 0.232 | 6.361 | 0.822 | 4.79 | 2.04 |
| 1.3 | 2.913 | 0.199 | 6.313 | 0.822 | 5.23 | 1.96 |

Analizirajući prethodne odzive na step poremećaj, može se uočiti da je metoda ŠEMA 1 efikasnija u odnosu na metodu ŠEMA 2, što zadovoljava kriterijum Shinskeyog [12], po kom kvalitetan industrijski regulator mora da bude podešen tako da, na step poremećaj na ulazu, daje minimum IAE i minimum maksimalnog odstupanja  izlaza od nominalnog režima uz ograničenja na robusnost.

Na slici 7 je prikazana je odskočni odziv na step referencu po metodama zasnovanim na max(ki) i max(k) [11], za adekvatne podešljive parametre  i  usvojenu vremenska konstanta filtra na referencu .

Slika 7. Odziv na step referencu:

(- - -) metoda ŠEMA 1; (___) metoda  ŠEMA 2.

4. ZAKLJUČAK

PID regulatori su veoma zastupljeni u industrijskim procesima i primjenjuju se za široke klase sistema kako stabilne tako i na nestabilne. Otuda i potreba za traženjem najbolje rješenje u smislu optimizacione procedure PID regulatora. U radu je izvršena uporedna analiza dvije optimizacione metode za optimalno podešavanja parametara PID regulatora u cilju upravljanja nestabilnih procesa. Na osnovu rezultata simulacije može se zaključiti da metoda zasnovana na maksimizaciji proporcionalnog pojačanja daje bolje performanse sistema u zatvorenoj povratnoj sprezi (SAU) u odnosu na optimizacionu metodu zasnovanu na maksimizaciji integralnog pojačanja PID regulatora. Takođe se može zaključiti da za nestabilne procese podešljivi parametar  treba birati iz šireg skupa nego što to važi za stabilne procese.

ZAHVALNICA

Zahvaljujemo se mentoru dr Tomislavu B. Šekari koji nas je motivisao i davao stručne kritike pri izradi ovoga rada.

REFERENCE

[1]	S. Yamamoto and I. Hashimoto, "Present status and future needs: the view from Japanese industry", In Arkun and Ray, Eds., Chemical Process Control-CPCIV. Proc. 4th Inter. Conf. on Chemical Process Control, TX, 1991.

[2]	L. Desbourough, R. Miller, "Increasing customer value of industrial control performance monitoring––Honeywell’s experience", in: Sixth International Conference on Chemical Process Control, AIChE Symposium Series Number 326, Vol.. 98, 2002.

[3]	K. J. Åström, T. Hägglund, "Revisiting the Ziegler–Nichols step response method for PID control", Journal of Process Control, Vol. 14, pp. 635–650, 2004.

[4] M. R. Mataušek, G. S. Kvaščev, "A unified step response procedure for autotuning of PI controller and Smith predictor for stable processes", Journal of Process Control, Vol. 13, pp. 787-800, 2003.

[5] S. Skogestad, "Simple analytic rules for model reduction and PID controller tuning", Journal of Process Control, Vol. 13, pp. 291–309, 2003.

[6] K. J. Åström, H. Panagopoulos and T. Hägglund, "Design of PI controllers based on non-convex optimization", Automatica, Vol. 34, pp. 585-601, 1998.

[7]	H. Panagopoulos, K. J. Åström and T. Hägglund, "Design of PID controllers based on constrained optimization", IEE Proc-Control Theory Appl., Vol. 149, pp. 32-40, 2002.

[8]	C. Hwang, C-Y. Hsiao, Solution of non-convex optimization arising in PI/PID control design, Automatica, Vol. 38, pp. 1895-1904, 2002 .

[9]	B. Kristiansson, B. Lennartson, "Evaluation and simple tuning of PID controllers with high-frequency robustness", Journal of Process Control Vol. 16, pp. 91-102, 2006.

[10] A. Karimi, M. Kunze, R. Longchamp, "Robust controller design by linear programming with application to a double-axis positioning system", Control Engineering Practice, Vol. 15, pp. 197-208, 2007.

[11] T. B. Šekara, M. R. Mataušek, "A simple effective method to obtain a well-tuned PID controller", Journal of Process Control, Submited Paper, 2006.

[12] F. G. Shinskey, "How good are our controllers in absolute performance and robustness?", Measurement and Control, Vol. 23, pp. 114–121, 1990.

[13] S. Skogestad, I. Postlethwaite, Multivariable Feedback Control, Wiley, 1996.

[14] G. Syrcos, I. Kookos, "PID controller tuning using mathematical programming" Chemical Engineering and Processing, Vol 44, pp. 41-49, 2005.