# ANIMACIJA I VIZUELIZACIJA MEHATRONIČKIH SISTEMA U MATLAB-SIMULINK OKRUŽENJU II-DIO

# Slobodan Lubura1, Milomir Šoja1, *Goran S. Đorđević2,

# 1Elektrotehnički fakultet Istočno Sarajevo,2Elektronski fakultet Niš

# е -mail: milomirsoja@yahoo.com, slubura@gmail.com, gorandj@elfak.ni.ac.yu

Sažetak: U radu je opisan  postupak modeliranja svih komponenti jednog složenog mehatroničkog sistema u MATLAB/SIMULINK okruženju. Kao primjer složenog mehatroničkog sistema  uzeta je aparatura za proučavanje procesa motornog učenja u balističkim zadacima pogađanja mete. Izgrađeni  SIMULINK model aparature povezan je preko VR toolbox-a sa predhodno izgrađenim modelom aparture u virteulnom okruženju. Na ovaj način dobila se animacija i vizuelizacija dinamičkog ponašanja aparature.

Abstract: Modeling procedures of all the components of a complex mechatronic system in MATLAB/SIMULINK environment have been described in the thesis. Apparatus for studying motor learning process in ballistic tasks of target practice has been taken as an example of a complex mechatronic system. Constructer SIMULINK model of the apparatus was connected to previously constructed apparatus model in virtual environment via VR toolbox. In this manner were achieved both animation and visualization of dynamic behavior of the apparatus.

# 1.UVOD

Da bi se napravila vizuelizacija bilo kog složenog mehatroničkog sistema pored modeliranja sistema u virtuelnom okruženju, potrebno je uraditi kinematičko i dinamičko modeliranje sistema u nekom sotverskom paketu za simulaciju dinamičkih sistema.  Danas se na tržištu može naći nekoliko softverskih paketa koji preko VRML specifikacije omogućavaju vizuelizaciju i animaciju sistema u virtuelnom okruženju.

Povezivanjem VRML objekata sa softverima za dinamičku modeliranje mehatroničkih i robotskih sistema, kao što su MATLAB, ANSIS, DYMOLA i sl. [5], omogućilo je jednostavno projektovanje simulatora na kojima se mogu testirati različiti algoritmi upravljanja. Ono što je nekada bilo dostupno samo specijalizovanim softverskih i hardverskim platformama, sada je postalo dostupno svima.

Za modeliranje složenog mehatroničkog sistema izabrano je MATLAB-SIMULINK okruženje. U radu je opisan postupak projektovanja SIMULINK modela simulatora aparature za proučavanje pokreta ruke u dinamičkim zadacima pogađanja mete, kao primjer jednog složenog mehatroničkog sistema.

2. PROJEKTOVANJE DIJELA SIMULATORA APARATURE U SIMULINK OKRUŽENJU

Na slici 1 prikazan je izgled aparature u virtuelnom okruženju. Nakon što je aparatura vjerno preslikana iz realnog u virtuelno okruženje, trebalo ju je “oživjeti” odnosno pojedinim elementima aparature dati stvarnu dinamiku pokreta, što je urađeno u MATLAB-SIMULINK okruženju [3]. Zadatak projektovanja simulatora u SIMULINK okruženju podijeljen je u nekoliko cjelina:

- sračunavanje komponenti leta loptice,

- sračunavanje početnih uslova leta loptice,

- generisanje signala dozvole i blokade integratora trajektorije leta loptice,

- detekcija loptice u kutiji i udara loptice u prepreku.

Slika 1. Virtuelna aparatura u V-Realm grafičkom okruženju

2.1 SRAČUNAVANJE KOMPONENTI LETA LOPTICE

Da bi se napravila vizuelizacija leta loptice na simulatoru, neophodno je sračunati njenu trajektoriju koja se može matematički opisati parametarskim jednačinama kosog hica po x i y komponenti:

,		(1)

gdje je -ubrzanje zemljine teže, a - konstante koje treba odrediti iz početnih uslova.

Na slikama 2 i 3 prikazana je realizacija navedenih parametarskih jednačina u MATLAB-SIMULINK okruženju.

Slika 2. Sračunavanje y-komponente trajektorije leta loptice

Slika 3. Sračunavanje x-komponente trajektorije leta loptice

Iako jednačine date sa (1) izgledaju trivijalno za modeliranje, problem je bio određivanje vremena aktiviranja i resetovanja integratora kojim se jednačine sračunavaju. Naime, dok se loptica nalazi u katapultu ona se kreće zajedno sa katapultom pa integratori za sračunavanje komponenti leta loptice moraju biti neaktivni. Trenutak  kada loptica napušta katapult određuje signal tenutak_izbacivanja_lopte kao što je označeno na slikama 2 i 3. Detaljan opis dobijanja navedenog signala dat je u nastavku ovog poglavlja. Od trenutka  integratori postaju aktivni, što znači da je loptica napustila katapult i po jednačini (1) kreće se ka meti. Kad y komponenta pozicije loptice dostigne vrijednost y=0, dolazi do resetovanja integratora i njihovog blokiranja, odnosno pripreme integratora za sračunavanje trajektorije leta naredne loptice. Da bi sve korektno radilo preko blokova enabled i upravljačkog signala enable na integratore dovode se odgovarajuće početne vrijednosti za integraciju.

2.2 SRAČUNAVANJE POČETNIH USLOVA TRAJEKTORIJE LETA LOPTICE

Da bi jednačina (1) bila potpuno određena potrebno je bilo sračunati nepoznate koeficijente. Pošto se radi o trajektoriji kosog hica koeficijenti imaju sljedeće vrijednosti:

,	(2)

gdje je - dužina katapulta, a - brzina i pozicija loptice i katapulta u trenutku izbacivanja loptice iz katapulta.

Sračunavanje navedenih koeficijenata i njihovo prosljeđivanje prema integratorima u odgovarajućim vremenskim trenucima realizovan je u bloku određivanje početnih trenutaka leta loptice koji je prikazan na slici 5.4.

Slika 4. Sračunavanje početnih komponenti trajektorije leta loptice

2.3 SIGNALI DOZVOLE I BLOKADE INTEGRATORA TRAJEKTORIJE LETA LOPTICA

Kako je već napomenuto da bi sve komponente potrebne za sračunavanje trajektorije kosog hica (1) bile korektno određene potrebno je na raspolaganju imati signal koji detektuje momenat izbacivanje loptice  (trenutak_izbacivanja loptice) i generiše se na osnovu signala ulazni reset. Ulazni signal za reset integratora ()snimljen je zajedno sa signalima

sa realne aparature.

Pored detekcije izbacivanja loptice iz katapulta, a da bi simulator korektno radio potrebno je u odgovarajućim vremenskim trenucima izvršiti resetovanje integratora i pripremiti početne vrijednosti integratora za generisanje naredne trajektorije leta loptice. Za resetovanje integratora koristi se složeni signal reset koji se dobija od snimljenog signala ulaznog reseta i dva unutrašnja interna signala reset1 i reset2 kako je prikazano na slici 5.

Slika 5 Generisanje signala dozvole i blokade integratora trajektorije leta loptice

2.4 DETEKCIJA LOPTICE U KUTIJI I UDARA LOPTICE U PREPREKU

Posljednji zadatak koji je trebalo izvršiti pri projektovanju simulatora u SIMULINK okruženju je detekcija pogotka mete, odnosno detekcija ubačenosti loptice u kutiju, kao i detekciju udara loptice u prepreku.

Problem je jednostavno riješen praćenjem trenutne pozicije leta loptice i generisanjem odgovarajućih reset signala. Za detekciju broja ubačenih loptica u kutiji upotrijebljen je brojač čiji se izlaz vidi na bloku display (broj ubačenih loptica). realizacija pomenutih funkcija detekcije loptice u kutiji i detekcije udara u metu prikazani su na slikama 6 i 7.

Slika 6. Detekcija udara loptice u prepreku

Slika 7 Detekcija loptice u kutiji

Konačan izgled svih elemenata simulatora povezanih u jednu cjelinu u MATLAB-SIMULINK okruženju prikazan je na slici 8.

Slika 8 Izgled simulatora u MATLAB-SIMULINK okruženju

3. ZAKLJUČAK

U radu je opisan  postupak modeliranja svih komponenti jednog složenog mehatroničkog sistema u MATLAB/SIMULINK okruženju. Kao primjer složenog mehatroničkog sistema  uzeta je aparatura za proučavanje procesa motornog učenja u balističkim zadacima pogađanja mete. Izgrađeni  SIMULINK model aparature povezan je preko VR toolbox-a sa predhodno izgrađenim modelom aparture u virteulnom okruženju. Na ovaj način dobila se animacija i vizuelizacija dinamičkog ponašanja aparature.. Opisana tehnika može poslužiti za projektovanje virtuelnih mehatroničkih i robotskih sistema, koji mogu biti sastavni elementi virtuelne laboratorije za mehatroniku, čije se usluge mogu koristiti preko WEB servisa.

4. LITERATURA:

[1] Criens C.H.A., T. ten Dam, Luijten H.J.C., Rutjes T.: “Building a MATLAB based Formula Student simulator“, Master Team Project report, Technische Universiteit Eindhoven Department Mechanical Engineering, Eindhoven, (June 20, 2006).

[2] Christian Schmid: “VCLAB - The Virtual Control Engineering Laboratory“, SYSID 2000, Symposium on System Identification Santa Barbara, California, USA, June 21 - 23, 2000.

[3] Danek Jan, Turevskiy Arkadiy, Denery Terry: “Simulation and Animation of Mechanical Systems“, American Institute of Aeronautics and Astronautics 2007.

[4] Domínguez Daniel: “VRML and Simulink Interface for the Development of 3-D Simulator for Mobile Robots”, Proceedings of World Academy of Science, Engineering and Technology Volume 25 November 2007.

[5] Dymola Multi-Engineering Modeling and Simulation [Online].Available: http://www.dynasim.se/.

[6] Ferretti Gianni, Magnani Gianantonio, Porrati Paolo, Rizzi Gianpaolo, Rocco Paolo, Rusconi Andrea: “Real-Time Simulation of a Space Robotic Arm“, IEEE 2008.

[7] Hoyer H., Gerke M., Masar I., Ivanov I., Röhrig C., Bischoff A.: “Virtual laboratory for Real-Time Control of Inverted Pendulum/Gantry Crane”, Department of Control Fern Universität in Hagen 2002.

[8] Paşc Ildiko, Ţarcă Radu, Popenţiu-Vlădicescu Florin: “The VRML Model and VR Ssimulation for a SCARA Robot”, ANNALS of the ORADEA UNIVERSITY. Fascicle of Management and Technological Engineering, Volume VI (XVI), 2007.

[9] Rãzmeritã Liana, Robin De Keyser: “Virtual Laboratory for Simulation and Control Engineering- A Design Perspective “,University of Galati, Romania; University of Gent, Belgium, 1999.

[10] Virtual Reality Toolbox™ 4, User’s Guide, The MathWorks, Inc. 2008.

[11] V-Realm Builder, User’s Guide and Reference, Ligos Corporation 1997.

[12] Tsepkovskiy Y., Antonov L., Kocev Cv., Palis F., Shoylev N.: “Development of a 3D and VRML Virtual Hand Models for Different Mechanical Gripper”, Journal of the University of Chemical Technology and Metallurgy, 43, 1, 2008, 159-164pp.