RF AND MICROWAVE FILTERS FOR MOBILE AND FIXED WIRELESS COMMUNICATIONS

D. BUDIMIR

Wireless Communications Research Group, Department of Electronic Systems,

University of Westminster, 115 New Cavendish Street, London W1W 6UW, United Kingdom.

budimid@wmin.ac.uk    http://www.cmsa.wmin.ac.uk/~budimid

# Abstract: - Tis paper presents the CAD of  RF and microwave filters such as lumped element, combline and waveguide bandpass filters for wireless communication systems. A new high-Q periodic resonator has been used for combline filter applications. Significant higher Q factor than conventional combline resonator in the same volume has been achieved.

Key-Words: - CAD, waveguide filters, combline filters. resonators, lumped element filters.

1. Introduction

When a common approach to the design of filters results in a design passband which differs considerably from that which is specified, optimization is required to tune the filter elements to achieve a design that meets certain requirements. Most RF and microwave filters have not yielded exact optimum synthesis. Taking into account parasitic effects, high frequency operation, frequency dependent elements, a narrow range of element values, and so on, a common approach to design provides, at best, only approximate answers. Not infrequently, a common approach may be used to great advantage in providing the initial points for optimization.

Lumped element, waveguide and combline filters have been widely used in RF and microwave wireless systems [3]  The backward of the current combline resonators is high loss, and makes its lower Q factor. A lot of researches were made in order to improve the Q factor of the conventional combline resonator. It is well known that Q factor can be improved by replacing its inner conductor with dielectric material. However, the dielectric loaded resonator has higher cost and poor spurious.

Periodic structure can make much smaller resonator [2] which employ the slow wave property of periodic structure to reduce the size of resonator. In this paper, we have designed combline filter with periodic N-disk mounted onto its inner conductor having clearly advantages for use at RF and microwave frequencies and demonstrated their applications in high-Q performance. Using this kind of combline resonator we can reduce the size of conventional combline resonator, or obtain higher Q than conventional combline resonator within the same volume.

2. Results

In order to illustrate our  approach, a fifth order lumped element generalized Chebyshev band-pass filters have been designed as first example. The band-pass filter can be described by 6 parameters: inductors (L1=L5, L2=L4, L3) and capacitors (C1=C5, C2=C4, C3) as marked in Figure 2. The return loss (solid line) and insertion loss (dashed line) calculated using the filter elements obtained on convergence are shown in Figure 3.

A five resonator X-band ridged waveguide Chebyshev bandpass filter, in which the widths of the ridges are arbitrarily chosen (see Figure 3), with passband specification LI(f) ( 0.05 dB,  9.30 GHz  ( f ( 9.80 GHz as second example has been design. The passband insertion loss (solid line) and return loss (doted line) calculated using the insert dimensions obtained on convergence are shown in the Figure 4.

Fig. 1. Generalized Chebyshev

band-pass filter

Fig. 2. Simulated Insertion and Return loss of generalized Chebyshev band pass filter

Figure 3. Configuration of a five resonator ridged waveguide bandpass filter

Figure 4. Calculated  insertion loss (solid line) and return loss (dashed line) of waveguide band-pass filter.

The schematic of two poles combline filter (see Figure 5) was designed with the novel resonators. It employs electric coupling by a gap between two resonators. We can adjust the height of the wall H, that is, the distance of the gap between the wall and enclosure to obtain the tuneable bandwidth.

Figure 6 shows the simulated insertion loss response and return loss. The filter has 53 MHz bandwidth and insertion loss of 0.15dB at the centre frequency of 3.10 GHz.

Fig. 6 Simulated insertion loss and return loss of the periodic 6-disk loaded combline bandpass filter

## 4. Conclusion

CAD of RF and microwave combline, waveguide and lumped element Chebyshev and Generalized Chebtshev band pass filters has been presented. A new periodic structure combline resonator has been used for combline filter applications. Significant higher Q factor than conventional combline resonator in the same volume has been achieved.

##### References

[1]	  Rhodes J. D. and S. A. Alseyab, “The

Generalized Chebyshev Low-pass Prototype Filter”  Mciowave Theory and Applications,Microwave Journal.,  September 1989, pp.197-201

[2] Kwok, R.S., Fiedziuszko, S.J., “Helical ceramic resonator structures”1999 IEEE MTT-S Int.  Microwave Symp. Dig., Vol: 3, pp: 1033 -1036 1999.

[3]  .Budimir, D., "Generalized Filter Design by Computer Optimization", ISBN 0-89006- 579-9, Artech House Books, 1998.

[4].  Gupta K. C, R.Garg and R.Chadha, "CAD of Microwave Circuits", Artech House, Dedham,MA,1981.

H

Fig. 5 Configuration of a two resonator combline filter.