APPLICATION OF INTERNAL MODELS IN THE DESIGN OF

DIGITALLY CONTROLLED ELECTRICAL DRIVES*

PRIMENA UNUTRAŠNJIH MODELA U PROJEKTOVANJU

DIGITALNO UPRAVLJANIH ELEKTROMOTORNIH POGONA

Milić R. Stojić, Faculty of Electrical Engineering, Belgrade

Milan S. Matijević, Faculty of Mechanical Engineering, Kragujevac

Abstract - The design of a controlling structure with internal models for digitally controlled electrical drives is given. In the control portion of the structure, the nominal model of the plant and model of immeasurable external disturbances are included to improve the system robustness and to extract the expected class of disturbances. Particular attention is paid to the design of IMPACT (Internal Model Principle and Control Together) structure for digitally controlled drives and a suitable modification of the structure is proposed in order to improve the system performance and to facilitate system synthesis.

Sadržaj – Daje se projektovanje upravljačke strukture sa unutrašnjim modelima za digitalno upravljane električne pogone. U upravljačkom delu strukture unose se nominalni model objekta upravljanja i model spoljnjeg nemerljivog poremećaja sa ciljem povećanja robustnosti sistema i eliminacije očekivane klase spoljnjih poremećaja. Posebna pažnja je posvećena projektovanju IMPACT (Internal Model Principle and Control Together) strukture digitalno upravljanih pogona pri čemu predlaže pogodna modifikacija strukture koja omogućava povećanje kvaliteta ponašanja sistema i pojednostavljuje sintezu sistema.

# INTRODUCTION

In many applications of controlled electrical drives the high dynamical performance and capability of the system to reject the influence of external disturbances on the steady-state value of the controlled variable are required. In the tracking regime, the tracking error is to be reduced to the level of sensor resolution, in the presence of the generalized disturbance that comprises the external disturbance and uncertainties of plant parameters. These requirements can be achieved by the design of IMPACT controlling structure (1-4( suited for the design of speed- and position-controlled electrical drives.

The IMPACT structure has the merits of both the structures based upon the IMP (Internal Model Principle) and IMC (Internal Model Control) (1,5(. As it is known, IMP means the inclusion of disturbance model into the controlling structure in order to compensate effects of expected class of external disturbances on the system output or the system controlled variable (angular speed or position of the motor shaft). The IMC structure is not suitable for disturbance rejection but it enables the achievement of the robust system stability and high dynamic performance.

In this paper, the conventional IMPACT structure is described and then its modification is proposed for application to the structural design of digitally controlled electrical drives. It will be shown that the application of predictive filters instead of disturbance observer, including the model of disturbance, gives the same or even better system performance. Unlike the structure with disturbance observer, the alternative control structure, proposed in this paper, is simpler and with a smaller number of tuning parameters within the internal models by which the robustness, filtering properties, and high dynamic performance of the system can be easily adjusted.

- PRINCIPLE OF ABSORPTION

Suppose that kth sample of an external disturbance  may be determined by a finite number m0 of previous samples. Then, the disturbance is regular and may be described by extrapolation equation (4(

(1)

where   is the prediction polynomial of order mo -1. Relation (1) is called the equation of extrapolation or prediction [4] and it may be rewritten as

(2)

where  denotes the z-transform of disturbance. Relation (2) is called compensation equation and FIR filter having the pulse transfer function  is the absorption filter or the compensation polynomial (4].

Absorption filter  is designed for a known class of disturbances and its impulse response becomes identically equal to zero after n sampling instants, where n ( mo. Hence, the compensation equation (2) may be considered as the absorption condition of a given class of disturbances. The condition can be expressed as

(3)

The extrapolation polynomial  is determined by an apriori information about disturbance  (4, 6], nevertheless, it is simply resolved as

(4)

In the case of a stochastic disturbance s(t), absorption filter (4) should suppress as much as possible effects of disturbance on the system output. Thus, for a low frequency disturbance s(t),  which can be generated by double integration of the white noise, an appropriate choice of absorption filter is  that corresponds to absorption of linear (ramp) disturbance (1, 7(. In majority of practical applications an appropriate choice might be . According to (4), prediction polynomial rejects ramp disturbances; but, it enables also the extraction of slow varying disturbances and even suppression of the effects of low frequency stochastic disturbances.

3. IMPACT STRUCTURE

In the IMPACT structure shown in Fig.1, the controlling process is given by its pulse transfer function or by polynomials  and , and the process dead-time given by integer k. Within the control portion of the structure in Fig.1 (shaded part) two internal models are included: the two-input nominal plant model

Fig.1.  IMPACT controlling structure

(5)

explicitly and the disturbance model embedded into the discrete filter . Both the internal nominal plant model and disturbance model is treated as the disturbance estimator. The control portion has two control loops that can be designed independently. The minor local control loop is designed by the proper choice of polynomials  and , while polynomials  and  in the main control loop are determined to achieve the desired system set point response. For a minimal phase plant, the proper choice of polynomial  is  (1(.

Under the nominal conditions  and for , the closed-loop transfer functions  and  are easily derived from Fig.1 as

(6)

and

.                     (7)

In virtue of (7), the system set-point response can be adjusted by determining appropriate polynomials  and  according to the desired system closed loop transfer function  Then, the absorption of an external disturbance and the speed of disturbance transient response are adjusted by choosing the structure and parameters of the disturbance estimator.

3.1. Elimination of disturbance

From (6), the steady-state error in the presence of a known class of external disturbance will become zero if

.

(8)

In the case of stable polynomial  and the plant of nonminimal phase,

(9)

and then the relation (8) is reduced to

.         (10)

As shown later, the stable polynomial  is to be chosen according to the desired speed of disturbance rejection and the required degree of system robustness and then polynomial  is determined to satisfy relation (10).

According to the principle of absorption, it is possible to design the observer estimator that rejects any kind of expected disturbances. To this end, consider the class of disturbances having the z-transform  Then, relation (10) is satisfied if the following Diophantine equation holds

(11)                                                  where  represents the absorption polynomial determined by . For example, to the polynomial and sinusoidal disturbances ( and ) correspond respectively  and , where  is the sampling period.

A unique solution of the Diophantine equation, which plays a crucial role in the design procedure of the observer estimator, proposed in this paper, does not exist (8(. Relation (11) is a linear equation in polynomials  and . Generally, the existence of the solution of Diophantine’s equation is given in [9]. According to [9], there always exists the solution of (11) for and  if the greatest common factor of polynomials  and  divides polynomial ; then, the equation has many solutions. The particular solution of (11) is constrained by the fact that the control law must be causal, i.e., . Hence, after choosing a stable polynomial  and degrees of polynomials  and , and inserting the absorption polynomial  that corresponds to an expected external disturbance, polynomials  and  are calculated by equating coefficients of equal order from the left- and right-hand sides of equation (11). Polynomial  obtained by solving (11) guarantees the absorption of the expected class of disturbances, while the choice of  affects the speed of disturbance rejection, system robustness, and sensitivity with respect to measuring noise. Good filtering properties and the system efficiency in disturbance rejection are the mutually conflicting requirements. Therefore, to reduce the noise contamination, the low-pass digital filter may be introduced to modify the internal model of the disturbance into

(12)

where  represents the pulse transfer function of the low-pass filter and  is a polynomial that satisfies  (11) and thus includes implicitly the internal model of disturbance. The lower bandwidth of the low-pass filter corresponds to a higher degree of system robustness and vice versa [10]. According to [10], complex disturbances require higher order of polynomial  and it will further reduce system robustness with respect to mismatches of plant parameters.

3.2. Parameter setting

The main control loop of the system of Fig. 1 is designed to achieve the desired set-point response determined by the system closed-loop transfer function

.                          (13)

According to (7), the desired closed-loop transfer function is achieved if the following identity holds

.                (14)

To satisfy (14), it is first necessary to solve the Diophantine equation

(15)

for polynomials  and  and then to determine the second polynomial of the main control loop of the system of Fig. 1 as

.                         (16)

where  in (15) is chosen as a stable polynomial. Recall that, for a minimal phase plant, .

The characteristic polynomial  is read from (13) or it may be determined by the desired closed-loop system pole spectrum. To improve the system robustness with respect to uncertainties of plant parameters, polynomial  may be extended by factors

.                         (17)

At the beginning, the values of  and integer n are to be chosen as small as possible and then they can be increased gradually until the required criterion of robust stability is satisfied. At the same time, polynomial   should be modified into

(18)

to save the achieved set-point response and to keep unchanged the steady-state value of the system output.

- MODIFIED IMPACT STRUCTURE

Fig. 2 shows the modified IMPACT structure for the control plants without transport lags, which may be applied for structural design of digitally controlled electrical drives  (1,2(. Signal wM  modeled the influence of load torque on system output  (angular speed or position of the motor shaft).

Fig.  2. Modified IMPACT controlling structure

The control plant of the structure in Fig. 2 is given by its nominal pulse transfer function

(19)

which is used as a two-input internal plant model within the control portion of the structure. Signal  estimates the influence of generalized disturbance on the system output.   Uncertainties of plant modeling may be adequately described by the multiplicative bound of uncertainties (11(

(20a)

.                 (20b)

Then, the system of Fig. 2 satisfies the condition of robust stability if the nominal plant is stable and if the following inequality holds

(21)

The robust system performance is achieved by the operation of the local loop of the structure in Fig. 2. Namely, the role of local loop is to suppress as much is possible the effects of generalized disturbance on the system output. According to the principle of absorption, it is necessary to include, into the control part of the structure, the internal model of disturbance having the input . In the case of control plant without the transport lag, the internal model of disturbance is reduced to the prediction polynomial . In Tsypkin’s works, most frequently the prediction polynomial

(22)

is proposed [3, 4]. This polynomial corresponds to linear disturbances but it effectively rejects different classes of slowly varying disturbances, too, especially in the case of small sampling period (1, 5(. According to the standard procedure of IMPACT structure design (5(, in the case of minimum phase plants,

(23)

is to be adopted. The main control loop of the structure in Fig. 2 is designed to achieve the desired pulse transfer function of the closed-loop system. Namely, by equating identically the desired  with

(24)

one can easily determine the polynomials  and  and thus the structure design is completed.

In the structure of Fig. 2 the encoder detecting the angular speed or position is not indicated. When the rezolver to digital converter (R/D) of limited resolution is applied, the measuring signal is contaminated by quantization noise (2(, which produces the fluctuation of control variable and losses in the motor. The predictive filter in the local loop increases the noise and that makes the system more sensitive to quantization of the speed and position. Therefore, the structure of Fig. 2 is modified by including the extended observer, as is shown in Fig. 3. The observer is extended by the model of disturbance to enable the estimation of angular speed in the case of the presence of a constant or slowlyy varying disturbance.

Fig.  3. Modified IMPACT structure of digitally controlled speed servomechanism

In this paper, for the extraction of disturbance, the simple polynomial predictor is applied in the local minor loop of the structure of Fig. 3, instead of internal model of disturbance used in the ordinary IMPACT structure of Fig. 2. Generally, the predictive filter is defined as an algorithm that estimates future values of the input signal and suppresses the noise contamination (12(. The relatively simple forms of digital predictive filters corresponding to polynomial disturbances are treated.

Suppose that signal  may be modeled by polynomial

(25)

where coefficients  are unknown real constants. For example, the pulse transfer function of Newton’s predictor, which estimates signal (25) with prediction horizon of p samples (i.e. ) has the form

.                            (26)

This filter estimates sample  by M+1 preceding samples . In the particular case of M = 1 and p = 1,  filter (26) becomes identical to prediction polynomial (22). Generally, when an electrical drive is under consideration (control plant has minimal transport lag) it is always p = 1. Filtering properties of the different Newton’s filters are illustrated in Fig. 4. Frequency characteristics of Fig. 4 show that noise components in the signal are increased when the order of the filter becomes greater. Therefore a linear approximation of signal (M = 1) may be adopted as an adequate, from the standpoint of noise sensitivity.

LSN (Linear Smoothed Newton) predictor (12(,  obtained by improving classical Newton’s, passes Mth difference of input signal through the low-pass digital filter . If the signal is adequately modeled by nth order polynomial, then the Mth difference of signal is constant and the necessity of its filtering is evident. In a general case, LSN predictor is given by pulse transfer function

(27)

Fig.  4. Frequency characteristics of Newton’s

predictive filter for  p = 1 and  M = 1, 2 and 3

For further simplification, the low-pass digital filter  may be adopted as a digital equivalent of the simplest low-pass analogue filter

(28)

having only one tuning parameter Tf of a clear physical meaning. By increasing the value of Tf  the better filtering properties and higher system robustness are achieved, especially within the low frequency band. On the other hand, with greater Tf  the speed of disturbance absorption is reduced and vice versa.

Fig.  5. Frequency characteristics of LSN predictor and prediction polynomial

For comparison, the frequency characteristics of the first order prediction polynomial and LSN predictor are illustrated in Fig. 5.

- ILLUSTRATIVE EXAMPLE

The efficiency of LSN predictor with Tf  = 0.2s, when compared with the application of prediction polynomial , in the case of IMPACT structure of positioning servomechanism is illustrated by Figs. 6 and 7. In the servomechanism, the 16-bits D/A converter and 12-bits R/D converter are applied. The results of simulation runs given in Fig. 6 (a) and (b) and Fig. 7 (a) and (b) are obtained by LSN predictor while the results in Fig. 6 (c) and (d) and Fig. 7 (c) and (d) are accomplished by the prediction polynomial. Notice that LSN filter suppresses the effects of quantization noise on the control variable and slightly slows down the speed of disturbance rejection. Sampling period T = 0.1s is assumed. The control plant is DC motor U12M4T having the electromagnetic gain factor K = 4.38 and mechanical time constant Tm  =  0.32s. The desired close-loop system transfer function is specified by two conjugate complex poles with undamped natural frequency (n = 2.5 rad/s and relative damping coefficient ( = 1.

Fig.  6. Operation of IMPACT structure in the absence of torque disturbance

Fig.  7. Operation of IMPACT structure in the presence of torque disturbance

The efficiency of LSN predictor application as a   prediction within the IMPACT structure of the speed-controlled electrical drive is illustrated in Figs. 8 and 9. The same DC motor U12M4T and T = 0.1s, as in the case of the positioning servomechanism, is applied. According to the proposed procedure, the desired closed-loop system transfer function

(29)

is specified and then the following polynomials of the control structure are calculated

, ,

,  (30)

and .

The system simulation is performed when 16-bits D/A and 12-bits R/D converters are applied (Fig. 8). The standard deviation of the difference between output signals generated with and without quantization noise, in the case of IMPACT structure with LSN predictor (Fig. 8), is 12% less than in the case of the observer based structure. By increasing time constant Tf , quantization noise is more suppressed but, at the same time, the speed of disturbance rejection is slowed down.  Hence, the implementation of LSN predictor instead of prediction polynomial gave approximately the same results as in the case of observer implementation in IMPACT structure, but the structure with LSN predictor is significantly simpler.  Furthermore, by tuning parameter Tf  it is possible, in a simple way, to adjust system dynamic properties, suppression of quantization noise, and to improve robust stability of the system.

Fig.  8. Responses of IMPACT structure of speed-controlled  servomechanism with LSN predictor (Tf   = 0.2s)

6.  CONCLUSION

The design procedure of IMPACT structure for digitally-controlled speed and position servomechanisms has been given. It was shown that the set-point response of the structure and speed of disturbance rejection could be adjusted independently. Instead of the design of disturbance estimator within the local loop of the structure, as in the case of basic IMPACT structure, different predictors are employed, for the purpose of disturbance extraction. This alternative approach has several advantages: the relatively easy setting of controller parameters, adjustable speed of disturbance rejection, and control of system robust stability.

- REFERENCES

(1( M.S. Matijević, “Razvoj novih struktura digitalno upravljanih elektromotornih pogona i industrijskih procesa”, Doktorska disertacija, Mašinski fakultet u Kragujevcu, 2001.

(2( M.R. Stojić, M.S. Matijević “Primena prediktivnih filtara umesto unutrašnjeg modela poremećaja IMPACT strukture“, Zbornik XLVI Konf. ETRAN-a, Teslić, 2002.

(3( (.З. Ц(пкин, “Синтез робастно оптимал(н(х систем управлени( об(ектами в услови(х ограничено( неопре-делености”, Автом. и Телемех., Но9, с. 139-159, 1992.

(4( Ya.Z. Tsypkin and U. Holmberg, “Robust stochastic control using the internal model principle and internal model control”, Int. J. Control, vol. 61, No4, P 809-822, 1995.

[5] M.R. Stojić, Lj.S. Draganović, and M.S. Matijević, (Survey and main features of control structures with internal models( (invited paper in Serbian), Proc. of XLIII ETRAN Conf., vol. I, pp. 211-220, Zlatibor, 1999, Yugoslavia.

[6] Ya.Z. Tsypkin and P.V. Nadezhdin, “Robust continuous control systems with internal models,” Control Theory and Advanced Technology, vol. 9, No.1, pp. 159-172, 1993.

[7] M.R. Stojić, M.S. Matijević, “Suppression of noise contamination in control systems with internal models,” Electronics, vol. 2, no. 1, pp. 33-42, 1998.

[8] K. Ogata, Discrete-Time Control Systems, Prentice-Hall, Inc., Englewood Cliffs, New Jersey, 1995.

[9] K.J. Åström and B. Wittenmark, Computer Controlled Systems: Theory and Design, Prentice-Hall, Inc., Englewood Cliffs, New Jersey, 1984.

[10] Stojić M , Matijević M., Draganović Lj., A robust Smith predictor modified by internal models for integrating process with dead time(, IEEE Transactions on Automatic Control, Vol. 46, No8, pp. 1293-1298, August 2001.

[11] Morari M., Zafiriou E., Robust Process Control, Englewood Cliffs, New Jersey, Prentice   Hall, 1989.

(12( S. V(liviita, S.J. Ovaska and Olli Vainio, (Polinomial predictive filtering in control instrumentation: A review(, IEEE Trans. on Industrial Electronics, vol. 46, No5, pp. 876-888, 1999.

# Footnotes

* This paper is an abridged version of the paper " APPLICATION OF INTERNAL MODELS IN THE DESIGN OF DIGITALLY CONTROLLED ELECTRICAL DRIVES " published in the journal Electronics.