OPTIMALNO PODEŠAVANJE PI REGULATORA ZASNOVANO

NA MAKSIMIZACIJI KOMBINOVANOG KRITERIJUMA JC

Tomislav B. Šekara, Miroslav R. Mataušek, Elektrotehnički fakultet u Beogradu

Sadržaj - U radu je razvijen postupak optimizacije PI regulatora zasnovan na maksimizaciji kombinovanog kriterijuma Jc. Izvršena je uporedna analiza sa najboljim do sada razvijenim metodama za podešavanje PI regulatora. Pokazano je da predložena metoda, u odnosu na prethodne,  poboljšava i  performanse i robusnost sistema u zatvorenoj povratnoj sprezi.

Abstract – A new procedure, based on the maximization of combined criterion Jc, is developed for PI controller optimization. Comparison with the best optimization methods proposed until now has been performed. It has been shown that the proposed method, compared to the other methods improves the closed- loop system performance and robustness.

Ključne riječi – PI regulator, Optimizacija, Robusnost

Key words – PI controller, Optimization, Robustness

1.	UVOD

Prema [1] oko 94% povratnih sprega u industriji realizovano je preko PI/PID regulatora, a istraživanje [2] je prema [3] pokazalo da u petrohemijskoj industriji taj procenat iznosi preko 97%. Ovakav značaj PI/PID regulatora bio je i motiv za dalji razvoj efikasnih i jednostavnih procedura za podešavanje parametara industrijskih regulatora [4,5]. S druge strane, posljednjih godina intenzivno se radi i na razvoju optimizacionih procedura  [6-12] kojima se parametri PI/PID regulatora određuju tako da se minimizira IAE (Integrated Absolute Error) pri ograničenjima na robusnost, što zadovoljava kriterijum Shinskeyog [13]. Po tom kriterijumu kvalitetan industrijski regulator mora da bude podešen tako da, na step poremećaj na ulazu, daje minimum IAE i minimum maksimalnog odstupanja  izlaza od nominalnog režima uz ograničenja na robusnost. Konačno treba pomenuti i mogućnost primjene savremenih metoda optimizacije kao što je  (mixed sensitivity) [14], kao i podešavanje PI/PID regulatora primjenom frakcionog prilaza [15-19].

U ovom radu se razmatra optimizacija PI regulatora s obzirom da je učešće ovog regulatora dominantno u naprijed navedenim procentima. Predloženi postupak zasnovan je na minimizaciji kombinovanog kriterijuma Jc. Izvršena je uporedna analiza predložene metode sa najboljim do sada razvijenim metodama za podešavanje PI regulatora. Pokazano je da predložena metoda kvalitativno potvrđuje ili poboljšava performanse sistema u zatvorenoj povratnoj sprezi: manji IAE i a robusnost je zagarantovana zahtjevom da maksimum osjetljivosti bude manji ili jednak zadatoj vrijednosti Ms .

Niz do sada razvijenih metoda [6-11] zasniva se na maksimizaciji integralnog pojačanja ki. Naime, ako je signal greške na jedinični step signal poremećaja pozitivan tada je

,				(1)

te maksimizacija ki vodi minimizaciji IAE.

Primjenom ovde predloženog kombinovanog kriterijuma Jc (maksimizacija integralnog pojačanja ki i maksimizacija propusnog opsega ( uz odgovarajući težinski faktor ()

, ,				(2)

optimizaciona procedura je poboljšana u smislu postizanja boljih performansi i robusnosti. Kroz niz simulacija na tipičnim procesima izvršeno je poređenje optimizacione procedure zasnovane na kombinovanom kriterijumu Jc sa optimizacionom procedurom zasnovanom na maksimizaciji integralnog pojačanja ki [6] i uočena je kvalitativna prednost.

2.	OPTIMIZACIONA PROCEDURA ZASNOVANA

NA MAKSIMIZACIJI JC KRITERIJUMA

Odaberimo upravljačku strukturu sa PI regulatorom prikazanu na slici 1, koju je predložio Åström [6]

Slika 1. Upravljačka struktura sa PI regulatorom

Funkcija povratnog prenosa ovakve upravljačke strukture je

.			(3)

Za stabilne procese upravljanja u odnosu na zadati podešljivi parametar  data je Nyquistova kriva na slici 2. koja u tački  tangira zadati krug poluprečnika  sa centrom u tački . U [6,7] u cilju postizanja željenih performansi kao podešljivi parametar usvaja se ,

Slika 2. Nyquistov dijagram  u odnosu na zadato Ms

Da bi primijenili sljedeću optimizacionu proceduru za određivane optimalnih parametara PI regulatora uz relaciju (3) neophodno je definisati funkciju

.			(4)

i zadati težinski faktor ( iz segmenta

Tada optimizaciona procedura dobija sljedeću formu:

Odredimo maksimum kombinovanog kriterijuma Jc

(5)

pod ograničenjima

,						(6)

,						(7)

za više vrijednosti ( iz intervala.

Rješavanjem prethodno definisane optimizacione procedure kao optimalni parametri PI regulatora

(8)

uzimaju se oni koji daju . Kako se radi o ograničenom segmentu pretraživanja parametra , jasno slijedi efikasnost date procedure u cilju određivanja optimalnih parametara PI regulatora. Napomenimo da se za , optimizaciona procedura svodi na optimizacionu proceduru datu u literaturi [6], čime su definisana i početna pogađanja ((, k, ki) za predloženu proceduru. Značajno poboljšanje performansi i robusnosti dobija se za (<1.

3.	REZULTATI SIMULACIJE

Za dvanaest procesa, korišćenih u [6,11], analizirana je predložena metoda zasnovana na maksimizaciji Jc. Detaljno upoređenje sa najboljim do sada razvijenim metodama prikazano je na slikama Sl.3 do Sl.14 , na kojima se uočava značajna prednost metode zasnovane na maksimizaciji Jc u odnosu na metodu zasnovanu ma maksimizaciji ki [6,9].

Slika 3. Odzivi na poremećaj za Gp1(s)

Slika 4. Odzivi na poremećaj za Gp2(s)

Slika 5. Odzivi na poremećaj za Gp3(s)

Slika 6. Odzivi na poremećaj za Gp4(s)

Slika 7. Odzivi na poremećaj za Gp5(s)

Slika 8. Odzivi na poremećaj za Gp6(s)

Slika 9. Odzivi na poremećaj za Gp7(s)

Slika 10. Odzivi na poremećaj za Gp8(s)

Slika 11. Odzivi na poremećaj za Gp9(s)

Slika 12. Odzivi na poremećaj za Gp10(s)

Slika 13. Odzivi na poremećaj za Gp11(s)

Slika 14. Odzivi na poremećaj za Gp12(s)

Prethodne slike predstavljaju odzive na poremećaj optimalno podešenog PI regulatora, za procese Gp1(s)  do Gp12(s), primjenom: metoda maksimizacija Jc - Šekara-Mataušek (ŠEMA) i metoda maksimizacija ki - Åström-Panagopoulos-Hägglund (APH), za Ms=2.

U predloženu proceduru optimizacije PI regulatora može se uključiti NF filtar u povratnoj grani, u cilju boljeg potiskivanja šuma. Vremenska konstanta filtracije Tf se uzima prema [6,7] saglasno relaciji

, ,				(9)

ili se računa i optimalna vrijednost Tf0 na osnovu zadatog Mn, odnosno maksimalne osjetljivosti na mjerni šum,

, .	(10)

Primjena relacije (10) znači da se u optimizacionu proceduru (5) – (7) uvodi dodatno ograničenje, a da je skup optimalnih parametara definisan relacijom (8) uz Tf= Tf0.

| Pr. | Ms | k | Ti=k/ki | (0 | IAE | Mp | ( |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 1.8 | 1.330 | 2.402 | 0.934 | 1.813 | 1.20 | 0.660 |
| Gp1 | 2.0 | 1.634 | 2.579 | 0.997 | 1.606 | 1.40 | 0.555 |
|  | 1.8 | 3.715 | 0.671 | 4.368 | 0.181 | 1.44 | 0.770 |
| Gp2 | 2.0 | 4.650 | 0.676 | 4.826 | 0.146 | 1.63 | 0.600 |
|  | 1.8 | 0.311 | 7.582 | 0.117 | 24.595 | 1.00 | 0.850 |
| Gp3 | 2.0 | 0.398 | 9.202 | 0.129 | 24.151 | 1.04 | 0.720 |
|  | 1.8 | 0.292 | 9.194 | 0.386 | 31.530 | 1.60 | 0.993 |
| Gp4 | 2.0 | 0.352 | 8.490 | 0.428 | 24.148 | 1.74 | 0.977 |
|  | 1.8 | 0.311 | 1.946 | 0.458 | 7.399 | 1.00 | 0.920 |
| Gp5 | 2.0 | 0.389 | 2.230 | 0.512 | 6.929 | 1.10 | 0.835 |
|  | 1.8 | 0.624 | 0.510 | 2.495 | 0.926 | 1.07 | 0.545 |
| Gp6 | 2.0 | 0.752 | 0.573 | 2.580 | 0.902 | 1.07 | 0.440 |
|  | 1.8 | 0.297 | 0.407 | 2.081 | 1.387 | 1.00 | 0.860 |
| Gp7 | 2.0 | 0.382 | 0.497 | 2.308 | 1.368 | 1.03 | 0.730 |
|  | 1.8 | 0.481 | 4.914 | 0.820 | 10.348 | 1.55 | 0.932 |
| Gp8 | 2.0 | 0.546 | 4.405 | 0.870 | 8.078 | 1.66 | 0.910 |
|  | 1.8 | 5.383 | 0.249 | 10.468 | 0.048 | 1.33 | 0.450 |
| Gp9 | 2.0 | 6.371 | 0.250 | 11.247 | 0.040 | 1.48 | 0.340 |
|  | 1.8 | 2.280 | 0.651 | 4.552 | 0.296 | 1.46 | 0.830 |
| Gp10 | 2.0 | 2.795 | 0.645 | 5.021 | 0.237 | 1.62 | 0.688 |
|  | 1.8 | 2.449 | 0.587 | 4.885 | 0.240 | 1.41 | 0.754 |
| Gp11 | 2.0 | 3.004 | 0.591 | 5.347 | 0.197 | 1.58 | 0.615 |
|  | 1.8 | 2.700 | 0.515 | 5.201 | 0.191 | 1.34 | 0.630 |
| Gp12 | 2.0 | 3.228 | 0.523 | 5.641 | 0.162 | 1.49 | 0.500 |

Tabela 1. Parametri optimalnog PI regulatora za 12 tipičnih procesa dobijeni na osnovu kombinovanog kriterijum Jc

4.	ZAKLJUČAK

Predložena nova metoda optimalnog podešavanja PI regulatora pokazala se izuzetno efikasnom za , dok se za  praktično svodi na optimizacionu metodu zasnovanu na maksimizaciji integralnog pojačanja ki. Efikasnost metode se praktično ogleda u boljim performansama uz bolju robusnost u odnosu na do sada najbolje rezultate dobijene u svijetu [6,9]. Analizirani kombinovani kriterijum se može upotrijebiti i za PID regulator uz adekvatna ograničenja što je predmet daljih istraživanja.

REFERENCE

[1]	S. Yamamoto and I. Hashimoto, "Present status and future needs: the view from Japanese industry", In Arkun and Ray, Eds., Chemical Process Control-CPCIV. Proc. 4th Inter. Conf. on Chemical Process Control, TX, 1991.

[2]	L. Desbourough, R. Miller, "Increasing customer value of industrial control performance monitoring––Honeywell’s experience", in: Sixth International Conference on Chemical Process Control, AIChE Symposium Series Number 326, Vol.. 98, 2002.

[3]	K. J. Åström, T. Hägglund, "Revisiting the Ziegler–Nichols step response method for PID control", Journal of Process Control, Vol. 14, pp. 635–650, 2004.

[4]	M. R. Mataušek, G. S. Kvaščev, "A unified step response procedure for autotuning of PI controller and Smith predictor for stable processes", Journal of Process Control, Vol. 13, pp. 787-800, 2003.

[5]	S. Skogestad, "Simple analytic rules for model reduction and PID controller tuning", Journal of Process Control, Vol. 13, pp. 291–309, 2003.

[6] K. J. Åström, H. Panagopoulos and T. Hägglund, "Design of PI controllers based on non-convex optimization", Automatica, Vol. 34, pp. 585-601, 1998.

[7]	H. Panagopoulos, K. J. Åström and T. Hägglund, "Design of PID controllers based on constrained optimization", IEE Proc-Control Theory Appl., Vol. 149, pp. 32-40, 2002.

[8]	C. Hwang, C-Y. Hsiao, Solution of non-convex optimization arising in PI/PID control design, Automatica, Vol. 38, pp. 1895-1904, 2002 .

[9]	B. Kristiansson, B. Lennartson, "Evaluation and simple tuning of PID controllers with high-frequency robustness", Journal of Process Control Vol. 16, pp. 91-102, 2006.

[10] A. Karimi, M. Kunze, R. Longchamp, "Robust controller design by linear programming with application to a double-axis positioning system", Control Engineering Practice, Vol. 15, pp. 197-208, 2007.

[11] T. B. Šekara, M. R. Mataušek, "A simple effective method to obtain a well-tuned PID controller", Zbornik radova 51 Konf. ETRAN, Vol. 1, 2007.

[12] T.B. Šekara, M.R. Mataušek, “Optimalno podešavanje PI/PID regulatora za procese definisane racionalnom funkcijom prenosa“, INFOTEH Vol. 6, Ref. A-2, p. 6-9, Jahorina Mart 2007.

[13] F. G. Shinskey, "How good are our controllers in absolute performance and robustness?", Measurement and Control, Vol. 23, pp. 114–121, 1990.

[14] S. Skogestad, I. Postlethwaite, Multivariable Feedback Control, Wiley, 1996.

[15] T. B. Šekara, Frakcione transformacije sa primjenom u sistemima automatike i električnim kolima, Doktorska disertacija, Elektrotehnički fakultet Univerziteta u Beogradu, 2006.

[16] I. Podlubny, "Fractional-Order Systems and  controllers", IEEE Trans. AC, Vol. 44, pp. 208-214, 1999.

[17] H. F. Raynaud and A. Zergaïnoh, "State-space representation for fractional order controllers", Automatica, Vol. 36, pp. 1017-1021, 2000.

[18] C. A. Monje, A. J. Calderon, B. M. Vinagre, Y. Q. Chen and V. Feliu, "On Fractional  Controllers: Some Tuning Rules for Robustness to Plant Uncertainties", Nonlinear Dynamics, Vol.38,pp. 369-381, 2004.

[19] T. B. Šekara, M. R. Mataušek, "Frakciono dinamičko proporcionalno dejstvo PI/PID regulatora", Zbornik radova L Konf. ETRAN, Vol. 1, pp. 252-255, 2006.

OPTIMAL TUNING OF PI CONTROLLER BASED

ON MAXIMIZATION OF COMBINED CRITERION JC

Tomislav B. Šekara and Miroslav R. Mataušek